Node: point_and_shoot_hovering_node
Function: Point towards a waypoint and drive underwater towards it using the yaw value from the IMU.
Package: point_and_shoot_hovering_update

Topics

Publishers
/heading_ctrl/heading [std_msgs/Float64] // calculated GPS heading to waypoint
/heading_ctrl/speed [std_msgs/Float64] // desired engine speed
/point_and_shoot_hovering_node/debug/target_distance [std_msgs/Float64] // Distance in m. to waypoint

Subscribers
/cc/ui/path [monsun_msgs/GpsPath]
/xsens/gps [monsun_msgs/Xsens700Position]
/xsens/imu [geometry_msgs/Vector3]

Services

/point_and_shoot_hovering_node/enable [std_srvs/SetBool] Enable/disable point_and_shoot_hovering_node node

Parameters (Launch)

enable: false
speed: 0.7 // desired engine speed
heading_threshold_degs: 1.0
        timeout_secs: 120.0
dist_to_waypoint_threshold_m: 3.0
    assumed_speed_m_p_s: 0.4
Files

Source
point_and_shoot_hovering_update.cpp
point_and_shoot_hovering_update_node.cpp

Launch
point_and_shoot_hovering_update_node.launch // launches point_and_shoot_hovering_node node only!

Description

The point_and_shoot_hovering_node node is used to perform the P&S behavior. In this the MONSUN points towards a GPS waypoint using the GPS positions and the compass (IMU yaw value) measurements. When the robot points in the waypoint’s direction, measured by a threshold value parameter and the distance to the waypoint is greater than a distance threshold, it starts to shoot or drives towards the waypoint by enabling the heading_ctrl service. The shooting continues until a timeout parameter or a calculating the time via assuming the robot’s speed underwater (launch parameter) whichever is less. Then when the robot surfaces again to correct the heading using GPS the actual speed over ground is calculated from the previous run and and then accordingly the new timeout is applied for the next run. The drift between the actual compass heading and the desired heading is also compensated for the next run. Also it is made sure that if the the robot crosses the waypoint and the distance is still greater than the distance threshold, the robot does not come back to the same waypoint but then goes to the next waypoint in the list. This is checked via comparing the initial calculated heading to further ones within a +/- 90 degrees range.